USB 1.1 Host Adaptor CF Card
CFU1U

Add USB 1.1 Host downstream port 
to your PDA

Expands your application and ideas
of  PDA based systems

Features

- Add USB 1.1 Host downstream port to your PDA.

- Only one and first USB Host Adapter CF card in the world.

- Works on Compaq iPAQ and Dell Axim, expands your application and ideas of PDA based systems.

- Attach bar code scanners, magnetic stripe card readers, keypads or other USB HID devices.

- Supports USB Flash Memory reader/writers, USB Flash Memory sticks, Zip, Mo and other removable storage devices. Allows to save, restore big data from/to your PDA, to exchange big data simply with WindowsPC.

- Easy to install, fully compatible with Windows Microsoft ActiveSync.

- 100mA USB Bus-Power is available at the USB port, don't need AC adapters for Low-Power USB devices such as Keypads, Flash Memory reader/writers, Bar code scanners or USB Flash Memory sticks.

- Low power consumption allows a long battery life.

System Requirements
One free CF TypeII compatible slot.

OS
- Pocket PC 2000 or Pocket PC 2002.
* ActiveSync and WindowsPC with CD-ROM drive are required to install the drivers into PDA.

Certified PDA and USB devices

PDA

Compaq : iPAQ with CF Jacket, PC Card Jacket.

Dell : Axim

Fujitsu : Pocket Loox

USB device

HID class devices :

Keyboards, Bar code scanners, Magnetic stripe card readers, RF-ID tag readers

Mass Storage devices :

USB Flash memory stick, ZIP drive, Removable HDD, Flash Memory card reader/writers

Specifications

| Product name | USB 1.1 Host Adapter CF Card |
| --- | --- |
| Product Number | CFU1U |
| Bus Interface | CF+ and Compact Flash Specification Rev.1.4 compliant |
| USB port interface | USB 1.1 compliant, supports Full(12Mbps) and Low(1.2Mbps). |
| USB port Connector | Series A female (down stream). |
| USB Bus-Power availability | 100mA(5V) maximum. |
| Physical Dimensions | CF TypeII 42.8(W) x 36.4(L) x 4.9(H) mm 1.69(W) x 1.43(L) x 0.13(H) inch |
| Cable length | 300mm(12 inch) |
| Weights | CF Card : 10g. 0.35oz. Cable : 20g. 0.7oz. |
| Power Consumption | Standby 5V Vcc 27mA(Not included USB Bus power output current). 3.3V Vcc 34mA(Not included USB Bus power output current). |
| OS Support | Pocket PC 2000, Pocket PC 2002. |
| Certification | VCCI/FCC Part 15, Class B. |
| Warranty | Removable Cable 90 days, Card 5 years. |
| Package includes | CFU1 USB 1.1 Host Adapter CF card. Removable cable. Software CD-ROM < Software CD-ROM contents > -USB Host driver and INF file. -USB Device Class drivers(HID, MassStorage) For Pocket PC 2000 and Pocket PC 2002. User's Guide |

*Covered and licensed by U.S.patents 4,603,320 4,686,506 4,972,470.